## Slide 1: Basic printing/slicing
By Friend

## Slide 2: Pre-workshop
Watch: 3D printing overview https://www.youtube.com/watch?v=f5fBwppxtkI
Watch: Fused Deposition Modelling (FDM) Process https://www.youtube.com/watch?v=J4OQQ9bA6g0
Watch: Original Prusa i3 MK3 guide for a new user https://www.youtube.com/watch?v=GE-lrRbU124
Read: Ultimaker guide to fixing common print issues
https://support.3dverkstan.se/article/23-a-visual-ultimaker-troubleshooting-guide

## Slide 3: Pre-workshop
Download and install:
  Cura https://ultimaker.com/en/products/ultimaker-cura-software
  Github Desktop https://desktop.github.com
Make a Github account

## Slide 4: If there’s a word you don’t understand in the slide, let me know and I’ll add it here

## Slide 5: Agenda
3D printing overview
Slicing
Starting a print on the printer
Cleaning the bed / sanding
General good practice
First layer importance
Printed solid
Troubleshooting

## Slide 6: Part 1: on the computer

## Slide 7: Quiz #1 (to get over the boring stuff)
What is 3D printing?
What is FDM?
What is slicing?

## Slide 8: Answer #1
3D printing is rapid prototyping method, mostly used in industry to save time and money
FDM is a way to 3D print, by layering plastic on top of each other
Slicing cuts a 3D model into a set of 2D layers for FDM

## Slide 9: Get repo
There’s two repo I want you to get today
  https://github.com/UBC-Rapid/Cura-settings
  https://github.com/rprakitpong/RapidPrototypingWorkshop
Click on the green button -> [Open in Desktop]
Github Desktop should pop up and you can click along to get download the whole repository to your laptop
If this is the first time you open Github Desktop, you’ll be prompted to log in

## Slide 10: Get repo
These repo act exactly like normal folders and files to you
I encourage you to read ahead on workshops if you have time
Click [Fetch Origin] occasionally to update your local repos

## Slide 11: Find a model
You’ll get to print a small model today (yays!)
Go to “thingiverse.com”
Search for something you want
  Some ideas: pen cap, loaded dice, lowpoly dog, low poly dog, utility knife, cable clip, cable wrapper

## Slide 12: Find a model
Once you click on the thing you want, scroll down and click on “Thing Files”
Get just the model you want
  Sometimes if you blindly download you’ll get a huge zip file with everything

## Slide 13: Cura
Opening Cura for the first time should let you add a printer
Select Prusa i3 Mk2

## Slide 14: Cura
We’re going to change print profile to what the team has tested
Click [Custom]
Click [Profile] -> [Manage Profiles]

## Slide 15: Cura
Click [Import]
Find the profile “MK2 Cl0ned PLA” and import it
  Or profile for other printer
  I’ll tell you which profile to import
Select the profile and click [Activate]

## Slide 16: Cura
Click on the folder icon on top left to import a model
Select the model you downloaded earlier
Right mouse drag to rotate camera, middle mouse drag to translate camera
Click on the model to select it for manipulation
Below folder icon are the tools to manipulate the model
Orient your model to maximize the chance of a successful print
  Eg: no long overhang
Try out a few of them
  It’s too simple for me to go over them

## Slide 17: Cura
Switch back to recommended print setup
Stick to recommended for now since it’s all preset by the profile you just import
I highly encourage you to look at the custom settings and see what you can customize for the printer through software

## Slide 18: Cura
Click [Prepare] to slice the model
Make sure the model you’ve found doesn’t exceed 15g
  Don’t be wasteful!
You can hover over time and material use to see in depth stats
Cura likes to give underestimate for time though
  Do that time multiplied by 1.25 as a ballpark
Click [Save to File] to save it to an SD card
  I’ll pass one around

## Slide 19: Quiz #1.5
If you increase length by twice, and the model is uniformly scaled, by how much does the volume increase?

## Slide 20: Answer #1.5
8 times (2^3)

## Slide 21: Part 2: on the printer

## Slide 22: Space tour
Team desktop
There’s Cura with all the settings on here

## Slide 23: Space tour
Work bench
Make sure it’s clean after you use it
  So not looking like this lol

## Slide 24: Space tour
Our printers
You’re free to use it for your own personal projects
You’ll use them throughout the workshops
You can keep things in cabinets
  Ask for passcode from execs

## Slide 25: Space tour
Tools cabinet
Put things back when you’re done

## Slide 26: Note
Wear PPE
Don’t eat in the space
Clean up after yourself

## Slide 27: Quiz #2 (to get over the boring stuff)
How do you measure the proper gap between first layer and printer bed?
What type of alcohol do you clean the bed with?

## Slide 28: Answer #2
A sheet of paper
Isopropyl alcohol

## Slide 29: Before Using the Printer – Changing Filament
Check to make sure the loaded filament is what you want
If it is right, good
To Change Filament (ABS/PETG -> PLA)
Preheat the printer to the temperature of the higher melting point
Hang the PLA on the printer
Scroll to the change filament setting and start feeding in the PLA
Continue until the extruded colour is fully changed

## Slide 30: Using the printer
Turn it on
Clean bed as needed
Put in SD card
Scroll to your gcode file
Preheat (or auto preheat)
Apply glue to the bed
Calibrate (or auto calibrate)
Watch until the first layer is done
  If it looks like the hot end is too high or low, scroll to “live z adjustment” and change the height
No point in explaining more, I’ll show you once and let you do your own

## Slide 31: Your turn
Before the next workshop or right after this workshop is done, I’ll let you into this space to print the model you sliced
You’ll clean bed/print successfully without my help
You can use online references though
  Prusa Mk3 Guide video I made you watch before this workshop is a good resource

## Slide 32: Troubleshooting
You’ll learn as you use the printer more
Simply: if it sounds unusual, if it vibrates, if something pops off, turn off the printer (red power switch) because something’s wrong
Google is your friend, but know when to stop
If it’s getting too complicated, put the issue on Slack, and ask senior members to help you with it
  Examples of issue getting too much: you have to get inside control box to fix, takes more than a day, you need power tools, etc.
  Doesn’t mean you’re off the hook, it just means you need to ask for help
Don’t break things too much
  You’ll be that senior member fixing stuff newbies break

## Slide 33: Some further readings
By the time this workshop ends, I’ll have put up a list of active projects and who the lead on that is
Use the project name as keywords and Google about it
As a member you’ll take part in projects, so it’s good to think a bit ahead
Take a brief look at the projects ideas slides in this repository
You’ll do a short project / work on a Rapid project at the end of workshops, so it’s good to see ahead and know what type of project you’ll do for which workshop you like